# Light Source Brightness Comparisons

- The following is provided only as a guideline and is not a strict requirement. However, please consider the area, usage, and target customers of your product when selecting the number of panels.

(1) Standard (Rigid) Panel Types

| Bulb Type | Specifications | # of OLED Panels needed to produce equivalent lumens |
| --- | --- | --- |
|  | Wattage (W) | Luminous Flux (lm) | 140X140mm Panels | 100X100mm Panels | 200X50mm Panels | 53X55mm Panels |
| Candle | 10W | 100 ~ 120 | 1 ~ 2 | 1 ~ 2 | 5 ~ 6 |
| A-Bulb | 60W | 580 ~ 720 | 4 ~ 5 | 8 ~ 10 | 30 ~ 36 |
| MR16 | 50W | 520 ~ 650 | 3 ~ 4 | 7 ~ 9 | 26 ~ 32 |
| EL | 13W | 620 ~ 800 | 4 ~ 5 | 8 ~ 10 | 30 ~ 40 |
| FPL | 26W | 1,400 ~ 1,800 | 9 ~ 12 | 20 ~ 24 | 70 ~ 90 |
| FL | 32W | 2,000 ~ 2,600 | 12 ~ 18 | 26 ~ 34 | 100 ~ 130 |

(2) Special (Flexible, Transparent) Panel Types

| Bulb Type | Specifications | # of OLED Panels needed to produce equivalent lumens |
| --- | --- | --- |
|  | Wattage (W) | Luminous Flux (lm) | Bendable Type (200 X 50 Panel Size) | Transparent Type (53 X 55 Panel Size) |
| Candle | 10W | 100 ~ 120 | 1 ~ 2 | 10 ~ 12 |
| A-Bulb | 60W | 580 ~ 720 | 8 ~ 10 | 60 ~ 70 |
| MR16 | 50W | 520 ~ 650 | 7 ~ 9 | 50 ~ 60 |
| EL | 13W | 620 ~ 800 | 8 ~ 10 | 60 ~ 80 |
| FPL | 26W | 1,400 ~ 1,800 | 20 ~ 24 | 140 ~ 180 |
| FL | 32W | 2,000 ~ 2,600 | 26 ~ 34 | 200 ~ 250 |

# LG Chem OLED Panel Specifications & Dimensions

| Panel | Optical Data |
| --- | --- |
| Type | Size (Luminance Area) | Thinness (mm) | CCT* (K) | Lumen** (lm) |
| Standard | Rigid | 100 X 100mm (90 x 90mm) | 1.90 | 4,000 | 75 |
|  |  |  | 1.90 | 3,500 | 75 |
|  |  |  | 1.10 | 3,000 | 75 |
|  |  | 140 X 140mm (129 x 129mm) | 1.10 | 3,500 | 155 |
|  |  | 200 X 50mm (140 x 40mm) | 1.90 | 4,000 | 73 |
|  |  |  | 1.90 | 3,500 | 73 |
|  |  | 53 X 55mm (46 x 46mm) | 1.90 | 4,000 | 20 |
| Special | Flexible | 200 X 50mm (140 x 40mm) | 0.20 | 4,000 | 73 |
|  | Transparent | 53 X 55mm (46 x 46) | 1.00 | - | ~ 10 |

- The flexible panels have a bending (not twisting) radius of up to 50mm (the distance between each edge when bent).

- The transparent panels have a transparency rate of 50%.

- Please check the specifications of the OLED Panels that you plan to use for your design.

- Please consider the luminance area as well as the panel size, and apply them to your design.

- Check http://www.lgchem.co.kr/lgchemoled/index.jsp for more information.

# Lighting Terminology

* Lumen (luminous flux, lm) : A measurement of light emitted by a lamp.

As reference, 60-watt incandescent lamp emits about 720 lumens.

** CCT (Correlated Color Temperature, k) : The color of the light source.

By convention, yellow-red colors (like the flames of a fire) are considered warm, and blue-green colors (like light from an overcast sky) are considered cool.

Color temperature is measured in Kelvin (K) temperature.

Higher Kelvin temperatures (3600–5500 K) are considered cool and lower color temperatures (2700–3000 K) are considered warm.